Modeling of radar scattering from oil films
Dr. Nicolas Pinel*, Dr. Christophe Bourlier
University of Nantes – IREENA Laboratory, Nantes, France
*E-mail: nicolas.pinel@univ-nantes.fr
air
oil
sea

---
Introduction: Context
General context of the study:
Remote sensing of oil slicks on sea surfaces
Better oil slick detection (& characterization and quantization)
 More effective direction of oil spill countermeasures
Modeling of the EM scattering
from oil slicks on sea surfaces
 Integration in imagery simulators
EM scattering → Normalized Radar Cross Section (NRCS)
NRCS 
  - one single interface → air/sea interface:
    relatively well-known
  - two interfaces → air/oil and oil/sea interfaces:
    research in progress
scattered power
incident power
air
oil
sea

---
Introduction: Purpose
Different possible approaches:
rigorous	asymptotic
+ ‘exact’	+ fast
- extensive computing time	- restricted domain of validity
- extensive memory space
MoM accelerated by
PILE+FB+SA
[Déchamps et al., IEEE TAP, 2007]
1. GOA (Geometric Optics Approx.)
+ intuitive approach (Thin Layer)
2. SSA-1 (Small Slope Approximation)
+ intuitive approach (Thin Layer)
3. etc.
 Statistical description of studied natural surfaces (hydrodynamic modeling)
cf. oil slick detection

---
Outline
Introduction
Hydrodynamic modeling (surfaces)
  - Natural interfaces: Statistical description
  1. Case of clean and contaminated sea surfaces
  1. Spectrum of clean and contaminated surfaces
NRCS of clean and contaminated seas
Conclusion & Future work

---
II.2. Case of clean and contaminated sea surfaces
Clean sea → Qualitative description:
Gravity and capillary waves:
Gravity waves:
- Large roughness h,l
Long correlation Lc,l
Capillary waves:
- Small roughness h,s
- Short correlation Lc,s
h,l
h,s
Lc,s
Lc,l
Several roughness scales
Sea surface
air
sea

---
II.2. Case of clean and contaminated sea surfaces
Contaminated sea → Qualitative description:
Damping of capillary waves
of both surfaces (air/oil and oil/sea)‏
Gravity waves:
- Large roughness h,l
Long correlation Lc,l
Capillary waves:
- Smaller roughness h,s
- Short correlation Lc,s
h,l
h,s
Lc,s
Lc,l
Yet damping dependent on various parameters (hydrodynamics)‏
air
oil slick film
sea
H

---
II.3. Spectrum of clean and contaminated surfaces
Height spectrum S(k=2/xd,) → Modeling:
  - Clean sea surface:
    Elfouhaily et al. surface spectrum model [Elfouhaily et al., JGR, 1997]:
    - Semi-empirical model
    - Consistent with Cox & Munk experimental model
      [Cox and Munk, JOSA, 1954]
      → RMS slope s
  - Contaminated sea (air/oil and oil/sea surfaces): few results:
    Lombardini et al. damping model [1] (Marangoni damping coefficient):
    - Independent of the oil film thickness H
    - Simple to use: 2 hydrodynamic parameters (oil)
  - Jenkins et al. damping model [2]:
    - Dependent on the oil film thickness H
    - Harder to use: 8 hydrodynamic parameters (oil)
  - ...
[1]: [Lombardini et al., JAOT, 1989]
[2]: [Jenkins and Jacobs, PF, 1997]

---
II.3. Spectrum of clean and contaminated surfaces
Lombardini et al. spectrum [1,3]: Independent of the oil film thickness H:
k² S(k)‏
Parameters relative to
the oil type:
 - D (characteristic pulsation)
- E0 (elasticity modulus)
Clean sea surface
In agreement with experimental results:
[Ermakov, BIS Symposium, 2008]
[Sergievsakaya and Ermakov,
BIS Symposium, 2008]
[Cox and Munk, JOSA, 1954]
k=2/xd
Surface wavenumber (rad/m)
[1]: [Lombardini et al., JAOT, 1989]
[3]: [Pinel et al., TGRS, 2008]
Gravity waves:
Weak damping
Capillary waves:
Significant damping
Slope spectrum isotropic part (dB)

---
II.3. Spectrum of clean and contaminated surfaces
RMS slopes ss: Comparison with experiments [4]
  - Cox & Munk model [4]: experiments conducted for H~0.02mm
  - Lombardini et al. model
Cox & Munk model
vs.
Lombardini et al. model:
Similar qualitative and quantitative results
Oil → significant damping of slopes
[4]: [Cox and Munk, JOSA, 1954]

---
Outline
Introduction
Hydrodynamic modeling (surfaces)
NRCS of clean and contaminated seas
  1. Contaminated sea: Thin film of identical parallel interfaces
  1. Numerical results: Validation of the thin-film approach
  1. Thin-film approach: Validity domain study
Conclusion & Future work

---
III.1. Contaminated sea: Thin film of identical parallel interfaces
At radar frequencies:
Values of relative permittivities (rsea, roil):
  - Sea relative permittivity rsea: relatively well-known
  - Oil relative permittivity roil: only a few results of the literature, but…
    at radar frequencies f: roil only weakly varying with f, as well as with T
OK for EM modeling / Pb. for oil type characterization (→ optical frequencies)
Homogeneous oil slicks (not emulsions):
Applicable to wind speeds u10 <~ 8-10m/s
Use of the Lombardini et al. damping model:
Surfaces assumed to be identical and parallel:
air
sea
oil

---
III.1. Contaminated sea: Thin film of identical parallel interfaces
Use of the height spectrum S(k) for an EM model:
Comparison between a rigorous method [5] (MoM+PILE+FB+SA)
and an asymptotic method using an intuitive approach
Oil films:
2 identical and parallel	surfaces
+ Low to moderate	thicknesses
+ Damping of capillary	waves
      Application of the thin-layer (“TL”) approach to an asymptotic model:
GOA-TL, then SSA1-TL, ...
[5]: [Déchamps et al., IEEE TAP, 2007]
oil
sea
Locally flat parallel interfaces (← capillary wave damping)‏:
From a double interface problem to a single interface problem:
	, with

---
III.2. Numerical results: Validation of the thin-layer approach
Simulation parameters:
  - Radar frequency f:
  - Wind speed (at 10 meters above the surface) u10:
  - Incidence angle i:
  - Oil film (wD = 6 rad/s, E0 = 9 mN/m) of thickness H:
  - Monte-Carlo process (PILE+FB): N = 50 realizations:
u10 = 5 m/s (Beaufort scale 3–4: light breeze – gentle breeze)
i = {0; -20} deg.
H = {10; 1} mm
Surface length: L = 250 0
Sampling step: x = /10
rsea = 70 + 41j
roil = 2.25 + 0.01j
f = 1 GHz 
(l0 = 30 cm)

---
III.2. Numerical results: Validation of the thin-layer approach
Oil film thickness H=10mm – rigorous (PILE+FB) vs. GOA
Good agreement with reference method
around the
specular direction
 Sea (PILE+FB)
 Sea (GOA)
 Oil (PILE+FB)
  Oil (GOA)
 Oil-on-Sea (PILE+FB)
  Oil-on-Sea (GOA-TL)

---
III.2. Numerical results: Validation of the thin-layer approach
Oil film thickness H=10mm – rigorous (PILE+FB) vs. SSA1
Very good agreement
with reference method
for all scattering angles
 Sea (PILE+FB)
ooo	Sea (SSA1)
 Oil (PILE+FB)
 xxx	Oil (SSA1)
 Oil-on-Sea (PILE+FB)
+++	Oil-on-Sea (SSA1-TL)

---
III.2. Numerical results: Validation of the thin-layer approach
Oil film thickness H=1mm – rigorous (PILE+FB) vs. SSA1
Very good agreement
with reference method
for all scattering angles
 Sea (PILE+FB)
ooo	Sea (SSA1)
 Oil (PILE+FB)
 xxx	Oil (SSA1)
 Oil-on-Sea (PILE+FB)
+++	Oil-on-Sea (SSA1-TL)

---
III.2. Numerical results: Validation of the thin-layer approach
Oil film thickness H=1mm – rigorous (PILE+FB) vs. SSA1; i=-20deg.
Very good agreement
with reference method
for all scattering angles
[Pinel et al., TGRS, 02/2008]
 Sea (PILE+FB)
ooo	Sea (SSA1)
 Oil (PILE+FB)
 xxx	Oil (SSA1)
 Oil-on-Sea (PILE+FB)
+++	Oil-on-Sea (SSA1-TL)

---
III.3. Thin-layer approach: Validity domain study
Simulation parameters (H polarization):
  - Radar frequency f:
  - Wind speed (at 10 meters above the surface) u10:
  - Incidence angle i:
  - Oil film (wD = 10 rad/s, E0 = 2 mN/m) of thickness H:
  - Monte-Carlo process (PILE+FB+SA): N = 70 realizations:
u10 = 6 m/s (Beaufort scale 4: gentle breeze)
i = {0; -20; -40; -60} deg.
H = {15} mm
 H  {loil/13}
rsea = 76 + 70j
roil = 2.25 + 0.01j
f = 1 GHz 
(l0 = 30 cm)
Surface length: L = 137 0
Sampling step: x = /10

---
III.3. Thin-layer approach: Validity domain study
qi = 0°
qi = -20°
qi = -40°
qi = -60°

---
III.3. Thin-layer approach: Validity domain study
Simulation parameters (H polarization):
  - Radar frequency f:
  - Wind speed (at 10 meters above the surface) u10:
  - Incidence angle i:
  - Oil film (wD = 10 rad/s, E0 = 2 mN/m) of thickness H:
  - Monte-Carlo process (PILE+FB+SA): N = 70 realizations:
u10 = 6 m/s (Beaufort scale 4: gentle breeze)
i = {-60} deg.
H = {3; 15; 60; 120} mm
 H  {loil/67; loil/13; loil/3; loil/1.7}
rsea = 76 + 70j
roil = 2.25 + 0.01j
f = 1 GHz 
(l0 = 30 cm)
Surface length: L = 137 0
Sampling step: x = /10

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
Outline
Introduction
Hydrodynamic modeling (surfaces)
NRCS of clean and contaminated seas
Conclusion & Future work

---
Conclusions & Future work
Hydrodynamic modeling → Surfaces statistical description:
Use of a simple damping model (Lombardini et al.)‏
Surfaces of the contaminated sea assumed to be identical and parallel
Electromagnetic modeling:
Simple intuitive approach (→ Fabry-Pérot interferometer)‏
Radar NRCS: Application of this approach → GOA, SSA1; MoM
Validation by comparison with a reference numerical method
[Déchamps et al., JOSAA, 2006]
Oil slick detection possible (characterization and quantization: hard)
Thin-layer approach: Validity domain study
Future work:
More investigations of the thin-layer approach validity domain
Extension of the method to a 3D problem
Use of a more physical damping model for oil films

---
Modeling of radar scattering from oil films
Dr. Nicolas Pinel*, Dr. Christophe Bourlier
University of Nantes – IREENA Laboratory, Nantes, France
*E-mail: nicolas.pinel@univ-nantes.fr
air
oil
sea

---
II.1. Natural interfaces: Statistical description
Height distribution (PDF): ph()
Height spectrum: S(k=2p/xd,)
2 main description tools:
z
z = (x)
x
0
12
generally Gaussian
Gaussian
6h
ph()

0
6h
x2
xd
Lc
M2
M1
x1
Sea: much more complex…
W(xd)
xd
x1
Lc
h2/e
h2

---
III. Case of sea and oil slick surfaces
Jenkins and Jacobs [4,5]: dependent on layer mean thickness H:
Parameters relative to oil type:
8 parameters (fluid mechanics)
D = 11 rad/s, E0 = 25 mN/m
Identical
Stronger damping for
Lombardini et al. model
Gravity waves:
Weak damping
Capillarity waves:
Strong damping
[4]: [Jenkins and Jacobs, Physics Fluids, 1997]
[5]: [Pinel et al., TGRS, to be published, 03/2008]

---
II.1. Natural interfaces: Statistical description
Other statistical description tools:
  - Slope distribution ps()
  - Autocorrelation function W(xd) ( =FT-1 of surface height spectrum S(k,) )
  - Slope spectrum k² S(k,)
  - etc. (other derivatives of height spectrum)
Different types of distributions:
Simple distributions: Gaussian, etc.
Natural interfaces  more complex descriptions in general:
Clean / Contaminated sea surface → Statistical description:
  - Height distribution function ph(): ≈ Gaussian
  - Height spectrum: → much more complex…

---
II.3. Spectrum of clean and contaminated surfaces
Sea covered in oil → Choice for height spectrum S(k):
Lombardini et al. model: Independent of H
Representation of air/oil and oil/sea surface
  - heights and slopes:
Confirmation of damping of small-scale height parts of S(k)
Significant damping of slopes k² S(k)
 Clean sea surface
   D= 16 rad/s, E0= 1 mN/m
 D= 10 rad/s, E0= 2 mN/m
D= 1 rad/s, E0= 4 mN/m

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
V POLARIZATION

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm

---
III.3. Thin-layer approach: Validity domain study
H = 15mm
H = 120mm
H = 60mm
H = 3 mm