## Slide 1: Procedural cloudscapes
Antoine Webanck1, Yann Cortial2, Eric Guérin2, Eric Galin1
1 Université Lyon 1, CNRS, LIRIS, France
2 INSA-Lyon, CNRS, LIRIS, France
Notes: Hello everyone, and thanks for being here with me. My name is Antoine Webanck, I am a PhD student from the University of Lyon, in France. During this presentation, I will talk about my work on procedural cloudscapes.

## Slide 2
Introduction
1. Cloudscape model
2. Cloudscape morphing algorithm
Results
Conclusion
Notes: My presentation will be articulated as follow: [Here’s an outline of my presentation]
I will start by introducing the problematic and cover the related work.
I will then describe our cloudscape model,
and explain how our cloudscape morphing algorithm works
Then, I will show you some results,
before concluding, and focusing on limitations and future work.

## Slide 3: Real example
High diffuse clouds layer
Low cloud sheet cover
Convective towers
Procedural cloudscapes, Antoine Webanck et al.
Notes: To illustrate our problem, let’s take an example.
This is a photograph of a real cloudscape.
In this photograph, we can see different cloud features:
We can see some convective towers, CLICK
Under the base of the towers, we see a cloud sheet cover CLICK
And higher over the convective towers, we see more diffuse clouds forming a second cloud layer CLICK.
That’s an example of what we want to model and animate.

## Slide 4: Problem
Modeling and animation of large scale cloudscapes
User control
Scientific challenges
Define a 4D (3D + t) function
Authoring such a function is complex
Chaotic natural phenomena (thermodynamics, fluid physics)
Procedural cloudscapes, Antoine Webanck et al.
Notes: Our objective is to model and animate large scale clouds such as in the previous photograph.
But doing so, we still want to provide an intuitive control to the user.
Our problem can be seen as the definition of a function that maps from the 4D domain of space and time to the positive cloud density domain.
As you can imagine, authoring such a function is complex, even more considering the chaotic natural phenomena behind the clouds.

## Slide 5: Related work: atmosphere animation
Cloudscape
Planet atmosphere
Modeling
Animation
Chung-Min2011
Neyret1997
Cloud
Goswami2016
Liu2006
Dobashi2006
Dobashi2010
Miyazaki2001
Miyazaki2002
Neyret1997
Ebert1997
Miyazaki2001
Miyazaki2002
Harris2003
Withers2008
Dobashi2008
Dobashi1998
Dobashi2010
Dobashi2006
Our method
Simulation
Morphing
Procedural
Ebert1997
Our method
Procedural cloudscapes, Antoine Webanck et al.
Scale (m)
Notes: To tackle the challenging problems of modeling and animating clouds, some work has already been done in the field of Computer Graphics.
For the modeling CLICK, some methods simulate the formation of the clouds.
Other methods use examples such as user sketches or satellite images.
And there are also some procedural methods, which model clouds directly, with fractals and procedural noise.
But if we look at the scale of the modeled clouds, the majority of these methods are limited to one or a few isolated clouds CLICK.
Very few work has been done to model larger clouds formations, such as cyclones, at the scale of the planet atmosphere.
We lie in between, at the scale of what we called cloudscapes CLICK.
For the animation CLICK, the most popular solution is to simulate the evolution of the clouds.
The problem with a simulation is that it is hard to control, and it is an expensive process, which limits interaction.
On the other hand, some procedural methods propose to animate procedural noise details directly, or to morph clouds between specified shapes by interpolating cloud primitives.
We build upon these procedural animation and morphing techniques CLICK, to propose an efficient and intuitive morphing algorithm.

## Slide 6: Pipeline preview
Procedural clouds details
Atmosphere density field
a (p, t)
Morphing computation
Anisotropic Shortest Path
Optimal transport
Cloudscape generation
Generic control function
Keyframes
Wind field
Terrain
Environment
Feedback control loop
with
Procedural cloudscapes, Antoine Webanck et al.
Notes: I will now present an overview of the whole pipeline of our method.
As inputs, our pipeline needs : CLICK
a wind field, and a terrain heightmap to define the environment, and
keyframes to describe the state of the cloud layers at different times
The first step is the morphing CLICK, which computes animated control primitives, that interpolate the given keyframes according to the environment.
Note that, the animated primitives can be reinjected as keyframes, in a feedback control loop, allowing to edit them more precisely CLICK.
The second step is the generation of the cloudscape CLICK.
For each cloud layer, the animated primitives produced by the morphing are combined with procedural clouds details, to give the specific shapes to the clouds.
Independent layers are then all blended together.
The final output is the 4D density field function CLICK, which can be rendered by raymarching for instance.

## Slide 7
Introduction
1. Cloudscape model
2. Cloudscape morphing algorithm
Results
Conclusion
Notes: I will now explain what is our cloudscape model.

## Slide 8
Clouds names refer to their shape and altitudes
  Cumuliform clouds have prominent convective bulbs
  Stratiform clouds are almost homogeneous layers
  Cirriform clouds are high and look like hair
2 km
7 km
12 km
Cirrostratus
Stratus
Cumulus
Nimbostratus
Cirrus
Cirrocumulus
Altostratus
Cumulonimbus
Different clouds at different altitudes
Type | Range (km)
Cirrus | 1 to 2
Stratus | 0.2 to 0.8
Cumulus | 0.1 to 5
Cumulonimbus | 7 to 12
Altocumulus
Mammatus
Cumulonimbus
Cumulus
Cirrus
Stratus
Clouds in meteorology
Altocumulus
Procedural cloudscapes, Antoine Webanck et al.
Notes: To define our cloudscape model, we looked at the classification of clouds used in meteorology.
The clouds are classified and named according to their specific shape and altitude.
As you can see, the nature produces multiple types of clouds with intricate shapes.
Each shape is already difficult to model by itself, it is even more challenging to combine multiple types of clouds, and to animate them.

## Slide 9: Global cloudscape model
Cloud density function
Each cloud type in a different layer
  altitude range
  wind field
  control function
  shape and details functions
Cloud density function of layer
Blend of all layers
Altitudes ranges
Wind conditions
Procedural cloudscapes, Antoine Webanck et al.
Notes: Let me remind you that we want to define the cloud density function .
I will now explain how we chose to define this function.
Inspired by the classification of clouds, we considered each cloud type separately and defined it in its own layer CLICK.
To each layer we associate specific attributes:
an altitude range CLICK
a wind field CLICK
And we define specific functions that I will describe later CLICK:
a control function
And some shape and details functions
Thus, we have one density function per layer CLICK.
The global cloud density function is then simply a blend of all the layers functions CLICK.
Recall that we want to define a cloud density function 𝑎(𝐩,𝑡):ℝ^4→ℝ^+.
Similarly to the clouds classification used in meteorology, we consider each cloud type separately.
We thus put each cloud type in a totally independent layer of associated altitude range, wind field and shape details functions.
We denote the cloud density function of layer i as 𝑎_𝑖 (𝐩,𝑡):ℝ^4→ℝ^+.
All layers are blended together as a sum to obtain the global cloud density function.

## Slide 10: Control function
Large-scale control function for the cloud cover
Defined manually for special effects
Defined with primitives for morphing
Primitives parameters
  Maximum density
  Position
  Radius
Position
Density
Radius
Control primitive
Control function
Primitives
EG logo
Contrails
Heart
Hole
Cover special effects
EG
Procedural cloudscapes, Antoine Webanck et al.
Notes: For simplicity, we now consider a single layer.
The goal of the control function is to control the presence or absence of clouds at a high level for this layer.
It can be seen as a cloud density function without details.
A control function can be defined manually for special effects such as carving specific shapes or holes in the clouds.
[Here CLICK, you can see some examples of such special effects.]
In order to apply a morphing method to the control function, we define it as a sum of spherical control primitives CLICK.
Each primitive has some parameters CLICK.
maximum density reached only at its center, decreasing with a smooth falloff function
center position
radius
Now you know how the smooth control function is defined, but it is not enough to obtain clouds with a detailed shape.
[Sure, with a lot of primitives, you could achieve some details but it would be very memory consuming.]
Even worse, it would become tedious to define lots of primitives which is the opposite of a high level control tool.
The control function goal is to control the presence or absence of clouds in at high level.
It can be seen as a cloud density function without details.
A control function can be defined manually for special effects such as carving specific shapes or holes in the clouds.
Here CLICK, you can see some examples of such special effects.
In order to apply a morphing method to the control function, we define it as a sum of spherical control primitives.
Each primitive has parameters of:
maximum density reached only at its center, decreasing with a smooth falloff function 𝑠(𝑥)
center position
Radius
Now you know how the smooth control function is defined, but it is not enough to obtain clouds with a detailed shape.
Sure, with a lot of primitives, you could achieve some details but it would be very memory consuming.
Even worse, it would become tedious to define lots of primitives which is the opposite of a high level control tool.

## Slide 11: Clouds shape and details
Control function and procedural noise
Smooth control function
Large shape
Smaller details
c and f
c, f and d
c
Procedural cloudscapes, Antoine Webanck et al.
Notes: The high level control function is smooth, it lacks the detailed features that characterize a cloud type CLICK.
To solve this problem, we enrich the control function with procedural noise.
The large-scale shapes are defined by composed of several octaves of noise of low frequency CLICK.
The smaller details are encased in with higher frequencies CLICK.
Please see the full paper for detailed examples of the procedural noises combined to model some specific types of clouds.
The high level control function is smooth, it lacks the detailed features that characterize a cloud type.
To solve this problem, we enrich the control function with procedural noise.
The large-scale shapes are defined by 𝜙(𝐩,𝑡) composed of several octaves of large frequency while the smaller details are encased in 𝛿(𝐩,𝑡) with higher frequencies.
Please see the full paper for detailed examples of the procedural noises combined to model some specific types of clouds.

## Slide 12
Introduction
1. Cloudscape model
2. Cloudscape morphing algorithm
Results
Conclusion
Notes: I will now explain how our morphing algorithm works.

## Slide 13: Cloudscape morphing
Animate each cloud layer separately
Morph between subsequent keyframes primitives
1. Trajectories computation
2. Trajectories selection
3. Ghosting
4. Interpolation
Procedural cloudscapes, Antoine Webanck et al.
Notes: In the definition of the cloudscape model, we used a time varying control function composed of animated control primitives.
I will now detail how our morphing method creates such a control function from given keyframes.
The morphing algorithm consists in four main steps :
1) CLICK The computation of trajectories and costs between each pair of initial and final primitives.
2) CLICK The selection of a subset of trajectories to link initial and final primitives.
3) CLICK The creation of ghost primitives to replace expensive trajectories.
4) CLICK The interpolation of primitives.

## Slide 14: Step 1: trajectories computation
Compute all anisotropic shortest paths
  Sample the XY domain
  Discretize time between keyframes in time steps
  Define anisotropic cost function between subsequent samples
  Anisotropic shortest path between subsequent samples
Procedural cloudscapes, Antoine Webanck et al.
Notes: The first step of the morphing is to compute the trajectories that will be used for interpolating control primitives.
Given two subsequent keyframes A and B composed of initial and final primitives CLICK, a terrain CLICK, and wind conditions CLICK, we compute all the anisotropic shortest paths CLICK between initial and final primitives.
To do so,
1) We sample the XY domain over the terrain CLICK.
2) We then discretize the time between the two subsequent keyframes in time steps CLICK.
3) Define an anisotropic cost function between subsequent samples CLICK.
3) Apply the Dijkstra algorithm to this implicit graph CLICK.
Now, we will detail the definition of the cost function as it is a central component of our method which will guide the creation of primitives trajectories.
Given initial and final primitives, a terrain, and wind conditions, we compute all the anisotropic shortest paths 𝜌_𝑖𝑗^∗ between initial primitive i and final primitive j.
To do so, we :
1) Sample the XY domain.
2) Discretize the time between the two subsequent keyframes in n time steps.
3) Apply the Dijkstra algorithm to this implicit graph with an anisotropic metric kappa.

## Slide 15: Step 1: anisotropic cost function
Anisotropic cost function
Elevation range
Simplified terrain
Wind
Terrain slope and elevation
Angle
Drag distance
Overlap cost
Slope cost
Procedural cloudscapes, Antoine Webanck et al.
Notes: Our goal when defining the cost function is to account for the environment conditions when building trajectories.
That’s why we express as a linear combination of three specialized cost functions.
CLICK is accounting for the divergence [or detour] of the trajectory from the trajectory obtained by following the wind.
It considers the distance of the detour and its angular deviation.
CLICK accounts for the terrain slope, adding cost when climbing and elevation.
And adds more cost to the areas that are more overlapping with the cloud layer.
The cost function 𝜅 gives the cost between two nodes of the Dijkstra graph.
Our goal when defining the cost function was to account for the wind conditions and the terrain during the computation of the morphing trajectories.
That’s why we express 𝜅 as a linear combination of three specialized cost functions: 𝜅_𝑤 accounting for the wind CLICK, and 𝜅_𝑠 and 𝜅_𝑒 to take account for the terrain slope and elevation CLICK.
Now to detail 𝜅_𝑤, we express how a trajectory diverge from pure wind advection, by multiplying two components CLICK.
The right component accounts for the angular deviation to the wind direction CLICK.
The left component is simply the distance to the point dragged by the wind CLICK.
The product of these two anisotropic terms is also anisotropic CLICK.
Then, to represent the influence of a terrain on the trajectories, let us consider a cloud layer ranging between a and b CLICK.
We take the terrain and modify it a little to obtain a new height field denoted 𝐳 ̃(𝐩). Because we don’t think the interactions between the terrain and the clouds should be as detailed as the terrain, we start by smoothing the terrain. And because the lower parts of the terrain won’t interact with high clouds, we crop the lowest altitudes to the base of the cloud layer.
𝜅_𝑠 is then accounting for the slope of the modified terrain CLICK while 𝜅_𝑒 adds more cost malus to the regions that overlap more with the cloud layer CLICK.

## Slide 16: Step 2: trajectories selection
known trajectory costs
Compute mass of initial and final primitives and
Apply optimal transport to optimize cost per unit of mass
  Less than trajectories subset
  Masses
Discrete optimal transport
Procedural cloudscapes, Antoine Webanck et al.
Notes: The second step of our morphing algorithm is to select a subset of trajectories to interpolate the primitives between two keyframes.
It is important to restrain the number of interpolation trajectories and thus, the number of primitives, for performance reasons.
It also imposes to find the better fitting trajectories.
We already know each possible trajectory and its associated cost CLICK.
We then compute the normalized mass of each primitive CLICK.
We use the costs and masses as input of a discrete optimal transport method CLICK.
The optimal transport is a global optimization of the transport cost per unit of mass.
It outputs the limited subset of trajectories CLICK and mass ratios to transport the mass between the two keyframes CLICK.

## Slide 17: Step 3: ghosting
Ghost primitives of null density: appearing or vanishing primitives
Discard expensive trajectories
Extrapolate trajectories following the wind
  Backward (fade in)
  Forward (fade out)
Redistribute mass to ghost primitives and
Procedural cloudscapes, Antoine Webanck et al.
Notes: The third step of the morphing algorithm is the ghosting.
In this step, we create ghost primitives of null density that allow new primitives to appear or old primitives to vanish with fade-in or fade-out effects.
Because the optimal transport of the former step is a global optimization, it always finds a solution, even in very unrealistic conditions.
Consider two morphing primitives CLICK with a final primitive only reachable by going against the wind.
Thanks to the cost function , the only possible trajectory is very expensive, but it is the only solution to allow the morphing.
To solve this problem, CLICK we discard the chosen trajectory.
But doing so, we would also lost all the transported mass and the associated primitives.
That’s why we extrapolate two new and independent trajectories by following the wind:
CLICK backward in time,
CLICK and forward in time.
CLICK At the end of each extrapolated trajectory, we put what we called a ghost primitive, which is invisible because it has no density.
We then dispatch the discarded masses to the ghost primitives, on the extrapolated trajectories, CLICK which produces a fade-out of the initial primitive, while the final primitive fades-in.
The third step of the morphing algorithm is the ghosting.
Because the optimal transport of the former step is a global optimization, it always finds a solution, even in very unrealistic conditions.
Consider two morphing primitives CLICK with a final primitive only reachable by going against the wind.
Thanks to the cost function 𝜅, the only possible trajectory is very expensive, but it is the only solution to allow the morphing.
To solve this problem, CLICK we discard the chosen trajectory.
But doing so, we would also lost all the transported mass and the associated primitives.
That’s why we extrapolate two new and independent trajectories by following the wind:
CLICK backward in time,
CLICK and forward in time.
CLICK At the end of each extrapolated trajectory, we put what we called a ghost primitive, which is invisible because it has no density.
We then dispatch the discarded masses to the ghost primitives, on the extrapolated trajectories, CLICK which produces a fade-out of the initial primitive, while the final primitive fades-in.

## Slide 18: Step 4: interpolation
One primitive per trajectory
Interpolate
  Position following the trajectory
  Radius linearly
  Density linearly weighted by relative mass
Procedural cloudscapes, Antoine Webanck et al.
Notes: The fourth and final step of the morphing algorithm is the interpolation of the primitives.
For each trajectory involving mass, we create an interpolating primitive of interpolated parameters.
Its position follows the trajectory
Its radius is linearly interpolated
Its density is weighted by the relative mass of its associated initial, final or ghost primitives
CLICK

## Slide 19
Introduction
I. Cloudscape model
II. Cloudscape morphing algorithm
Results
Conclusion
Notes: I will now show you some results achieved with our method.

## Slide 20
Results – Cold front
Procedural cloudscapes, Antoine Webanck et al.
Clouds: 8 cloud types
Statistics: 8 control functions, no morphing
Notes: This is a footage showing a rain storm scenario, which is called a cold front in meteorology.
It features different types of clouds implemented in our model with procedural details.
You will see waves of clouds from the three families of clouds in addition to the heart of the storm: the Cumulonimbus.
[Cirrus, Altostratus, Altocumulus, Cumulus humilis, Stratocumulus, Cumulus congestus, and Cumulonimbus capilatus]

## Slide 21
Results – Cross winds
Procedural cloudscapes, Antoine Webanck et al.
Clouds: Stratocumulus and Cirrus
Statistics: 110 primitives, morphing in 81s
Notes: This footage features two cloud layers of lower Stratocumulus and higher Cirrus.
Each layer follows its associated wind which blows in opposite direction to the other.
[To model the layers control functions, we only used a total of 110 control primitives.
The morphing computation took 81 seconds.]

## Slide 22
Results – Good weather
Procedural cloudscapes, Antoine Webanck et al.
Clouds: Stratus and Cumulus
Statistics: 460 primitives, morphing in 68s
Notes: This footage shows stratus/fog dissipating while rising up, before some denser clouds start to appear.
It is an example of result obtained with a clever application of the ghosting, to create fade-in and fade-out effects.
[To model the layers control functions, we used a total of 460 control primitives.
The morphing computation took 68 seconds.]

## Slide 23
Conclusion
Procedural cloudscapes, Antoine Webanck et al.
Controllable procedural animated cloudscape
  Efficient model with procedural details
  Controllable by intuitive key-framing
  Coherent morphing accounting for environment
Notes: To sum up, our method allows to model and animate cloudscapes.
Our procedural model is efficient,
The keyframes provide intuitive temporal control,
The animation is coherent and accounts for the wind conditions and terrain,
And the ghosting process lets the user compromise between blind morphing which can go against environment conditions, and pure advection by following the wind.

## Slide 24
Stratocumulus over the Pacific Ocean, NASA
Future work
Procedural cloudscapes, Antoine Webanck et al.
More types of clouds
Inter-layer morphing
Planet scale
Notes: Nevertheless, there is still room for improvements:
We could add more types of clouds to our procedural model.
We would like to design morphing between different layers.
The morphing of the primitives from different layers is trivial, but it is not the case of the procedural details of two different types of clouds.
And finally, just have a look at the background. It is photograph of showing plenty of Stratocumulus at the scale of the Earth.
A cloudscape modeled with our method would only be a tiny part of these cloud formations.
It would be interesting to model at the higher scale of the planet atmosphere and to design some Level Of Details tools.
THANK YOU FOR LISTENING!

## Slide 25: Procedural cloudscapes
Antoine Webanck1, Yann Cortial2, Eric Guérin2, Eric Galin1
1 Université Lyon 1, CNRS, LIRIS, France
2 INSA-Lyon, CNRS, LIRIS, France