## Slide 1: Real-time observer from stochastic reduced order model
M Ladvig, A M Picard, V Resseguier,
D Heitz, E Mémin, B Chapron

## Slide 2: Content
Context : observer for unsteady aerodynamism
Physics, data & reduced order model (ROM)
Simulation, measurements & data assimilation
Reduced order model under location uncertainty
Results
2

## Slide 3: PART I
Context :
Observer for unsteady aerodynamism

## Slide 4: application
Estimation and prediction:
Air flow
Lift, drag, AoA
…
Observer
Controller
Simple model
Simple model
Blade pitch
Fluidic actuators
…
Wind turbine sensors
LIDAR
E-penon
4
  Lower wind turbine maintenance costs
  Estimate and predict unsteady aerodynamism -- in real-time –
  for better active control loops
Which simple model? How to combine model & measurements?
Wind
turbine
blade
Wind fluctuations
Damages
  Longer wind turbine life cycle

## Slide 5: PART II
Physics, data & reduced order model

## Slide 6: Reduced order model (ROM)
Time
Space
Parameters
(if any)
Solution of an PDE with the form:
 | Full space | Reduced space
Solution coordinates |  | 
Dimension |  | 
 | Full space | Reduced space
Solution coordinates |  | 
Dimension |  | 
Order of magnitude examples in CFD
6

## Slide 7: POD-Galerkin
Principal Component Analysis (PCA) on a dataset to reduce the dimensionality:
Resolved modes
Snapshots
Spatial modes
PCA
Off-line
simulations
Approximation:
 ROM for very fast simulation of temporal modes
Projection of the “physics” onto the spatial modes :
( Physical equation (e.g. Navier-Stokes))

## Slide 8: PART III
Simulation, measurements & data assimilation

## Slide 9: Combining simulations and measurements
Numerical
Simulation
(ROM)
   erroneous
On-line
measurements
   incomplete
   possibly noisy
9
Velocity
More accurate
estimation
globally in space
Data assimilation
( particle filtering
with tempering & mutation )
Need for uncertainty / errors quantification
Random dynamics

## Slide 10: Part IV
Reduced order models under location uncertainty

## Slide 11: location uncertainty models (LUM)
Randomized Navier-Stokes model
__________________
Good closure
Good model error quantification for data assimilation
Residual
Assumed
time-uncorrelated
SALT
LUM
Memin, 2014
Resseguier et al. 2017 a, b, c, d Cai et al. 2017
Chapron et al. 2018 Yang & Memin 2019
Crisan et al., 2017
Gay-Balmaz & Holm 2017
Cotter and al. 2018 a, b
Cotter and al. 2019
Holm, 2015
Holm and Tyranowski, 2016
Arnaudon et al. 2017
Mikulevicius & Rozovskii, 2004
Flandoli, 2011
References :
Cotter and al. 2017 Resseguier et al. 2019 a, b
Resolved modes
Randomized ROM

## Slide 12: Summary
Off-line : Building ROM
On-line :
Simualtion & data assimialtion
Stochastic
ROM
Randomized
Physics
(LUM)
Data
DNS code
Physics
(Navier-Stokes)
Stochastic
ROM
Flow
Temporal modes
Data
assimilation
(particle filtering)
Measurements

## Slide 13: Part V
Results :
UQ &
Fast Observer
of the flow

## Slide 14: Numerical results : 3D Wake at Reynolds 300
Reduced order models with degrees of freedom
only 1 PIV spatial point (local, blurred and noisy measure) is assimilated 10 times by vortex shedding cycle
Our method :
POD-Galerkin with Navier-Stokes under location uncertainty (LUM)
Reference : PCA-projection of the “true” simulation (-dof DNS) (Optimal from -dof linear decomposition)
State-of-art :
POD-Galerkin with Navier-Stokes + optimally tuned eddy viscosity & additive noise
Inflow
Q-criterion
Inflow
Q-criterion
Inflow
Q-criterion

## Slide 15: CONCLUSION
valentin.resseguier@scalian.com

## Slide 16: Conclusion
valentin.resseguier@scalian.com
Reduced order model (ROM) : for very fast and robust CFD ( degrees of freedom.)
  Combine data & physics (built off-line)
  Closure problem handled by LUM
Data assimilation : to correct the fast simulation on-line by incomplete/noisy measurements
  Model error quantification handled by LUM
First results
  Optimal unsteady flow estimation/prediction in the whole spatial domain (large-scale structures)
  Robust far outside the learning period
Next steps
Increasing Reynolds (reduced DNS  reduced LES)
Real measurements (PIV, Mems, …)
Increasing the degrees of freedom ()
Parametric ROM
  Now implemented in OpenFOAM / ITHACA-FV

## Slide 17: Bonus slides
valentin.resseguier@scalian.com

## Slide 18: Model under location uncertainty, The tracer Advection example
Advection
Diffusion
Drift
correction
Multiplicative
random
forcing
Balanced
energy
exchanges
Large scales:
Small scales:
Variance
tensor:
18

## Slide 19: Reduced models under location uncertainty: Galerkin projection gives SDEs for resolved modes
additive noise
multiplicative noise
n x M
M x 1
M x 1
1 x M
n x 1
(stochastic Navier-Stokes)
Large scales:
Small scales:
Variance
tensor:
2nd order polynomial:
coefficients given by physics,
and
Correlations to estimate

## Slide 20: Numerical results : 3D Wake at Reynolds 300
Reduced order models with degrees of freedom
only 1 PIV point (local, blurred and noisy measure) is assimilated 10 times by vortex shedding cycle
Our method :
POD-Galerkin with Navier-Stokes under location uncertainty (LUM)
Reference : PCA-projection of the “true” simulation (-dof DNS) (Optimal from -dof linear decomposition)
State-of-art :
POD-Galerkin with Navier-Stokes + optimally tuned eddy viscosity & additive noise
Inflow
Q-criterion
Inflow
Q-criterion
Inflow
Q-criterion

## Slide 21: Numerical results : 3D Wake at Reynolds 300
Reduced order models with degrees of freedom
only 1 PIV spatial point (local, blurred and noisy measure) is assimilated 10 times by vortex shedding cycle
n=2
n=4
n=8